## Slide 1
Chen long
Linux DTS 介绍

## Slide 2
目录
DTS背景与概念
DTS语法、工具与相关文件结构
DTS实例介绍
DTS相关代码分析
. 2

## Slide 3
. 3
. 3
DTS背景与概念
引入DTS之前的状况
  ARM平台使用hard code描述硬件资源。
  维护的痛苦，https://lkml.org/lkml/2011/3/17/492
  基于同一型号SoC的不同板子，需要不同的内核镜像。
如何解决上述问题？
    观察其它平台，X86与非X86系统。
    EFI与Open Firmware。

## Slide 4
. 4
. 4
DTS背景与概念
一些术语
  DTS ----- Device Tree Source，用于描述板级硬件资源的文本文件 ，扩展名是.dtsi或.dts 。
  DTB ----- Device Tree Blob，用于描述板级硬件资源的二进制文件 ，扩展名是.dtb 。
  DTC ----- Device Tree Compiler，用于将.dts文件编译转换成.dtb的编译器。

## Slide 5
. 5
. 5
DTS背景与概念
.dts文件
dtc
.dtb文件
kernel | .dtb | ramdisk
0x80008000
0x85400000
0x85500000

## Slide 6
. 6
相关工具
sprd-scx35l_sp9630ea.dts
dtc
dtbTool
dt.img
sprd-scx35l_sp9630ea.dtb
kernel(Image)
objcopy
vmlinux in ELF
root/
mkbootfs
minigzip
ramdisk.img
ramdisk
mkbootimg
boot.img

## Slide 7
. 7
DTB文件格式
struct boot_param_header
(alignment gap) (2)
memory reserve map
(alignment gap)
device-tree structure
(alignment gap)
device-tree strings
(1) Refer to setup.c for struct boot_param_header.
(2)alignment gaps并不是必须的，取决于各个数据块的对齐要求。

## Slide 8
. 8
DTB文件中的节点格式
* OF_DT_BEGIN_NODE (that is 0x00000001)
* for version 1 to 3, this is the node full path as a zero terminated string, starting with "/". For version 16 and later, this is the node unit name only (or an empty string for the root node)
* [align gap to next 4 bytes boundary]
* for each property:
* OF_DT_PROP (that is 0x00000003)
* 32-bit value of property value size in bytes (or 0 if no value)
* 32-bit value of offset in string block of property name
* property value data if any
* [align gap to next 4 bytes boundary]
* [child nodes if any]
*OF_DT_END_NODE (that is 0x00000002)
Device-tree structure:

## Slide 9
. 9
DTB初始化概览
u-boot从boot.img中装载.dtb到内存中,Refer to cmd_.cboot.c
2. kernel初始化时，扫描该.dtb数据，在内存中建立起相应的链表和树形结构，由of_allnodes 指向。Refer to unflatten_device_tree().
内核为每一个节点，向platform bus注册一个platform_device结构。Refer to of_platform_populate().
当平台驱动初始化的时候，向platform bus注册一个platform_driver结构，根据linux的驱动模型，该platform_driver结构将会与相应的platform_device结构关联。Refer to sprdfb_main.c.
Notes: boot.img存储在emmc或nand的’boot’分区中。

## Slide 10
. 10
sprd-scx35_sp7731gea.dts
gic: interrupt-controller@12001000 {
compatible = "arm,cortex-a15-gic", "arm,cortex-a9-gic";
#interrupt-cells = <3>; /* Determine if this can be a parent of INT controller */
#address-cells = <0>; /* Determine the length of address in reg property of this node only when there have no parent for this node. */
interrupt-controller; /* Identify INT controller */
reg = <0x12001000 0x1000>, /* Index 0 */
<0x12002000 0x1000>; /* Index 1 */
};
The linker put ‘IRQCHIP_DECLARE(cortex_a15_gic, "arm,cortex-a15-gic", gic_of_init);’ in irq-gic.c into the kernel according to the link script.
irqchip_init() in irqchip.c initializes the GIC according to the description in the DT.
[ The callback irq_init_cb in of_irq_init() ] < ===== > gic_of_init () in irq-gic.c.
address
size

## Slide 11
. 11
sprd-scx35_sp7731gea.dts
gic: interrupt-controller@12001000 {
compatible = "arm,cortex-a15-gic", "arm,cortex-a9-gic";
#interrupt-cells = <3>;
#address-cells = <0>;
interrupt-controller;
reg = <0x12001000 0x1000>,
<0x12002000 0x1000>;
};
timer{
compatible = "sprd,scx35-timer";
….
interrupts = <0 118 0x0>,
….
<0 121 0x0>;
};
不同于‘ #address-cells’，‘#interrupt-cells’仅仅修饰它的孩子节点的‘interrupts’属性
Refer to kernel\Documentation\devicetree\bindings\arm\gic.txt.
最后一个字段是flag，0x0表示 不支持irq_set_type()，而是使用初始化时设定的缺省配置， level triggered, active low.
SPI interrupts are in the range [0-987]. PPI interrupts are in the range [0-15].

## Slide 12
. 12
sprd-scx35_sp7731gea.dts
d_gpio_gpio: gpio@f5220000{
compatible = "sprd,d-gpio-gpio";
reg = <0Xf5220000 0x1000>;
gpio-controller;
interrupt-controller;
#interrupt-cells = <2>;
#gpio-cells = <2>;
gpiobase = <0>;
ngpios = <256>;
interrupts = <0 35 0x0>;
};
key_volumedown {
label = "Volumedown Key";
linux,code = <114>;
gpios = <&d_gpio_gpio 124 1>;
debounce-interval = <2>;
gpio-key,wakeup;
};
Label, optional, as phandle.
逻辑编号，用于sanity check以及可能的真实gpio编号计算，如out_gpio = gpiobase + gpio
124是offset，1是flag，具体意义由使用该gpio的模块代码定义。Refer to gpiolib-of.c

## Slide 13
. 13
sprd-scx35_sp7731gea.dts
i2c2: i2c@f5370000{
compatible = "sprd,i2c";
interrupts = <0 13 0x0>;
reg = <0xf5370000 0x1000>;
#address-cells = <1>;
#size-cells = <0>;
…
ltr_558als@23{
compatible = "LITEON,ltr_558als";
reg = <0x23>;
gpios = <&d_gpio_gpio 140 0>;
};
};
蓝色部分是用于描述i2c2 host.
红色部分是用于描述连接到i2c 2 host的client devices. reg=<0x23>，定义了该client的地址。Refer to of_i2c_register_devices().

## Slide 14
. 14
sprd-scx35_sp7731gea.dts
clk_gpu_axi: clk_gpu_axi {
#clock-cells = <0>;
clocks = <&clk_aon_apb>;
clock-output-names = "clk_gpu_axi";
};
gpu{
compatible = "sprd,mali-utgard";
clock-names= "clk_gpu_axi","clk_gpu","clk_153m6“, …;
clocks = <&clk_gpu_axi>,<&clk_gpu>,<&clk_153m6>, …;
};
1. of_clk_get_by_name(np, name):
根据name参数，在节点np的clocks-names属性中确定与name对应的index ===>根据index在clocks属性中找到相应的parent clock.
2. of_clk_get_parent_name(np, index):
根据index在节点np的clocks属性中找到相应的parent clock ，使用该parent clock成员中的参数作为index，在parent clock节点的clock-output-names中确定对应的clock name.
2. 也有例外，如fb0: fb@20800000 {};节点，其并未使用clocks和clock-names属性，而是使用了clock-src属性的值设置时钟。
clocks属性描述了该节点的所有parent clocks
clock-cells属性描述了，该节点的child clocks中clocks属性的每个成员的参数个数。如#clock-cells = <1>;
clocks = <&osc 0>, <&pll 1>;
clock-output-names属性描述了该节点的所有output cloks.
clock-names属性描述了该节点的所有input clocks(parent clocks)。

## Slide 15
. 15
sprd-scx35_sp7731gea.dts
fb0: fb@20800000 {
compatible = "sprd,sprdfb";
clock-names = "dispc_clk_parent", …;
clocks = <&clk_256m>, <&clk_256m>, … ;
clock-src = <256000000 256000000 384000000>;
dpi_clk_div = <7>;
sprd,fb_use_reservemem;
sprd,fb_mem = <0x9F956000 0x3AA000>;
};
Refer to dispc_clk_init() in sprdfb_dispc.c